# GPON ONU

# 4GE + WiFi

# & VoIP

AP214H Series

- ITU-T G.984 compliant

- GPON or EPON

- 4× GE port

- 1 × VoIP port

- 1x POTS

- 2x USB

- 802.11 b/g/n/ac WiFi

- Remote Management

- FTTH, FTTB, FTTO, PON + EOC

- Broadband Internet, VoIP, IPTV, VOD, IP Camera, WiFi

Ascent’s AP214H GPON HGU ONT is a GPON optical network unit designed to meet the requirements of broadband access networks. It is ideal for FTTH/FTTO applications to provide data, voice, and video services based on a GPON network.

The AP214H dual-mode ONU optical interface supports EPON and GPON access. The ONU automatically recognizes the central office OLT mode (GPON or EPON) and activates the corresponding PON mode, thereby completing GPON or EPON adaptive access.

The AP214H GPON HGU ONT is a dual-mode ONU designed to meet the needs of telecom and radio and television operators for FTTH fiber-to-home multi-service reception. This product integrates Gigabit Ethernet through mature, stable and cost-effective Gigabit XPON, Switching, WDM and HFC technology, have the characteristics of high bandwidth, high reliability, easy management and good quality of service (QoS) guarantee. The functions meet ITU-T, IEEE related recommendations, relevant international standards and technical specifications of industry standards, and have good compatibility when used with standard based central office OLTs.

## Key Features

Support EPON&GPON mode adaptive

Support GPON WAN port with 1.244Gbps uplink / 2.488Gbps downlink link

Support 4x 10/100/1000BASE-T Ethernet RJ45 Ports

Support 1x POTS

Support 2x USB

Support 802.11b/g/n speed up to 300Mbps

Support 802.11a/b/g/n/ac speed up to 867Mbps

## Application Diagram

Specifications

| System Parameter | Technical Index |
| --- | --- |
| Chip Model | RTL9607+RTL8192+RTL8812 |
| Memory | DDR3：256MB / FLASH 128MB |
| WiFi Chip | 2.4G&5G: RTL8192+RTL8812 |
| GPON Protocol Specification | Comply ITU-T G.984 GPON standard: G.984.1: General Characteristics G.984.2: physical Media Dependent (PMD) layer specifications G.984.3: transmission convergence layer specifications G.984.4: ONT management and control Interface specification: Support DS/US transmission rate to 2.488 Gbps/1.244 Gbps. Wavelength: 1490 nm downstream & 1310 nm upstream Comply with class B+ type PMD. Physical distance reach to 20 km. Support Dynamic Bandwidth Allocation (DBA). GPON Encapsulation Method (GEM) supports Ethernet packet Support GEM header removal/insertion and data extraction/ segmentation (GEM SAR). |
| Network Protocol Specifications | Support 802.3 10/100/1000 Base T Ethernet ANSI/IEEE 802.3NWay auto-negotiation 802.1Q VLAN tagging/un-tagging Support flexible traffic classification Support VLAN staking. |
| Interface | WAN: One Giga optical interface (APC or UPC) LAN: 4*10/100/1000 RJ-45 ports VoIP: 1*RJ-11 port USB: 2*USB |
| LED Indicators | Power, PON, LOS, 5G, 2.4G, LAN1-4, FXS, WPS, USB-1, USB-2 |
| WiFi Rate | 2.4G: 802.11b/g/n speed up to 300Mbps 5G: 802.11a/b/g/n/ac speed up to 867Mbps |
| Buttons | Power/WPS/WLAN/Reset |
| Antennas | 2*5dBi external antenna (dual band antenna) |
| Power Supply | DC12V/1.5A |
| Product Size | 156*130*186mm (length X width X height) |
| Work Environment | Working temperature: 0°C to 40°C Working humidity: 10% to 95% , no condensation |
| Security | WPA/WPA2/WPA3 Firewall, Dos Protection |
| WAN Networking | Static IP WAN connection DHCP client WAN connection PPPOE WAN connection |
| VOIP | G.711A/µ, G.729, and G.722 encoding/decoding T.30/T.38/G.711 fax mode |
| Management | Standard OMCI (G.984.4) Web GUI (HTTP/HTTPS) Firmware upgrade via FTP/TFTP/HTTP Telnet, Web, SSH CLI command via telnet/console Configuration backup/restore TR069 |

## Ordering Information

Product Name	Product Description

AP214H-GE-00-AC-S-2 	AP200H GPON CPE 1x GE (1.25G US, 2.5G DS ), 4xGE, 1xFXS, 1xUSB, 2.4G&5.8G WIFI b/g/n/ac, Single Fiber, SC/PC, PS included

## Contact Information

#### Ascent Communication Technology Ltd

AUSTRALIA	HONG KONG SAR

140 William Street, Melbourne	Unit 9, 12th Floor, Wing Tuck Commercial Centre

Victoria 3000, AUSTRALIA	177 Wing Lok Street, Sheung Wan, HONG KONG

Phone: +61-3-8691 2902	Phone: +852-2851 4722

#### CHINA	USA

Unit 1933, 600 Luban Road	2710 Thomes Ave

200023, Shanghai CHINA	Cheyenne, WY 82001, USA

Phone: +86-21-60232616	Phone: +1-203 816 5188

#### EUROPE	VIETNAM

Pfarrer-Bensheimer-Strasse 7a	15 /F TTC Building, Duy Tan Street

55129 Mainz, GERMANY	Cau Giay Dist., Hanoi, VIETNAM

Phone: +49 (0) 6136 926 3246	Phone: +84 243 795 5917

WEB: www.ascentcomtec.com	EMAIL: sales@ascentcomtec.com

Specifications and product availability are subject to change without notice. Copyright © 2023 Ascent Communication Technology Limited. All rights reserved. Ver. ACT_AP214H_GPON_ONT_Datasheet_V1d_Apr_2019